|  | Geotrack DiSEqC-Motor H-120 |  |
| --- | --- | --- |

| ArtNr.: 2386 |  | € 120.- |
| --- | --- | --- |

| DiSEqC 1.2 extremly low noise - compact and powerful DiSEqC 1.2 Easy to upgrade by only one coaxial cable weather proof and rust protection Backlash eliminated technical specification Protocol: DiSEqC 1.2 Compatible Receiver: Receiver with DiSEqC 1.2 or Interface Box Antenna Size: 120 cm max. Speed: 1,9°/sec (at 13 V); 2,5°/sec (at 18 V) Azimut Angle: 80° East ~ 80° West (160°) Elevation Angle: 25 ~ 75° Input Voltage: 13/18 Vdc Output Voltage: 13/18 Vdc Power Consumption: 50 mA (Standby), 200 mA (Normal), 350 mA (Max.) Satellite Positions: 60 Calibration Function: Yes (Go to 0°) Manual East/West Buttons: Yes (build-in on the bottom of the mount) Limit Protection: 1. Fixed type with micro switches 2. Programmable Software Limit 3. Current Limit Positioning Sensor: High Resolution Hall Effect Sensor Connector: F-type Weight (Mount): 3,1 kg / 3,5 kg (Gross) Dimension (Mount): 345 x 168 x 110 mm english manual |  |
| --- | --- |